## Slide 1: Robot Operating system ROS Navigation
Lecturer: Dr. Bui Ha Duc
Dept. of Mechatronics
Email: ducbh@hcmute.edu.vn

## Slide 2: History of ROS Navigation
Purpose of navigation: Navigate robot autonomously from starting point A to final goal B given a map of the environment
To navigate a robot we need:
  A map
  A localization module
  A path planning module
These components are sufficient if:
  The map fully reflects the environment
  The environment is static
  There are no errors in the estimate
However:
  The environment (map) changes
  Thing may appear in the path of the robot
  The sensor is noise

## Slide 3: History of ROS Navigation
The original ROS Navigation Stack was born around 2008–2010
It natively supported differential-drive and holonomic robots
It’s difficult top modify without breaking the whole thing

## Slide 4: History of ROS Navigation
Map provided by a “Map Server”
Planner has a layered architecture (local and global planner)
Obstacle sensing refined on-line by appropriate modules
Adaptive Monte Carlo Localization algorithm uses a particle filter to track the position of the robot

## Slide 5: Map
A map is a representation of the environment where the robot is operating
It should contain enough information to accomplish a task of interest
Representations:
  Metric
    Occupancy Grid Based (OGM)
    Feature Based
    Hybrid
  Topological
  Hybrid
Notes: Map files are stored as images, with a variety of common formats being supported (such as PNG, JPG, and PGM)

## Slide 6: Building a Map
ROS uses GMapping, which implements a particle filter to track the robot trajectories.
To build a map you need to:
  Record a bag with /odom, /scan/ and /tf while driving the robot around in the environment it is going to operate in
  Play the bag and the gmapping-node, and then save it.

## Slide 7: Robot Pose and Path
A metric map defines a reference frame
To operate in a map, a robot should know its position in that reference frame
A sequence of waypoints or of actions to reach a goal location in the map is a path

## Slide 8: Localization
ROS implements the Adaptive Monte Carlo Localization algorithm (ACML)
ACML:
  Relies on laser scan
  Use particle filter to track robot position
https://www.youtube.com/watch?v=NrzmH_yerBU

## Slide 9: Path Planning
Determine (if it exists) a path to reach a given goal location given a localized robot and a map of traversable regions.

## Slide 10: Mapping
Given a robot that has a perfect ego estimate of the position, and a sequence of measurements, determine the map of the environment.
A perfect estimate of the robot pose is usually not available.
Instead we solve a more complex problem: Simultaneous Localization and Mapping (SLAM).
SLAM= Simultaneous Localization and Mapping
Estimate:
  the map of the environment
  the trajectory of a moving device
using a sequence of sensor measurements.

## Slide 12: Navigation 2
Released in 2018
Nav2 is a complete rewrite designed to leverage the modern capabilities of ROS
  Architecture: From Monolithic to Modular
  move_base  Nav2 Servers
  Logic: From Finite State Machine (FSM) to Behavior Trees (BT)
  Complex mission logic can be defined in a simple XML file without recompiling code
  Lifecycle nodes for systematic launch
  Every major component in Nav2 has states like unconfigured, inactive, active and finalized
Notes: Navigation is split into independent Action Servers (Planner, Controller, Smoother, Behavior Tree). Each server is a separate node, making the system more stable and easier to debug or replace specific components

## Slide 13: Nav2 vs Nav

## Slide 14: Nav2 achitecture

## Slide 15: Behaviour Tree
Behavior Trees enable complex behaviors with less code and more modularity, making them easier to maintain and extend, compared to traditional state machines.
https://www.behaviortree.dev/

## Slide 16: ROS2 Lifecycle nodes
States:
Unconfigured= created or new
Inactive = ready to work
Active = doing real work
Finalized = ready to destroy
States are controlled through ‘change_state’ service

## Slide 17: Nav2 Plugin interface
The ‘nav2_core’ package contains abstract interfaces for plugins
Global Planner – global_planner.hpp
Local Planner – local_planner.hpp
Recovery behaviors – recovery.hpp
Goal checker – goal_checker.hpp
Exceptions – exceptions.hpp