## Slide 1: Robot Operating system Behavior Tree
Lecturer: Dr. Bui Ha Duc
Dept. of Mechatronics
Email: ducbh@hcmute.edu.vn

## Slide 2: Decision making
Problem:
Given a situation and set of possible actions to execute, which of the possible actions is the best?

## Slide 3: Task Switching Structure
Task Switching Structure is framework that decides which task to run given a set of available actions and changing environment conditions
  When a and what action do we switch
Traditional method: FSM – Finite State Machines
FSM Example for Cleaning robot
driving to the location of the item
transports the item to its destination
places the item at its destination

## Slide 4: Task Switching Structure
FSMs lack modularity, become less effective as tasks grow more complex

## Slide 5: Introduction to Behavior Tree
Behavior Tree (BT) is a Task Switching structure
BT Advantages:
  Graphical representation: Easier to understand the overall decision process.
  Modularity: Sub-trees can be reused easily.
  Hierarchical structure: Actions exist on many levels of detail
  Reactivity: Re-evaluated frequently, allowing fast reactions.

## Slide 6: Introduction to Behavior Tree
Usage of Behavior Tree and State Machine in Robotics
Source: https://arxiv.org/pdf/2208.04211

## Slide 7: Components of BT
Root: the starting point of the execution
Start the Logic (“tick” signal)
Has 1 direct child, usually a control Node
Receives a status back from its child
  Success, Failure or Running
Pass status back to the main controller

## Slide 8: Components of BT
Nodes: perform tasks
Types: Control, Decorator, Action and Condition
Nodes are define in C++ by users/developers
Node don't pass arguments to each other directly
Parent node can only see its direct child / children

## Slide 9: BT Nodes
Control Nodes – The Decision Makers
Can have one or more children
Return 3 status: Success, Failure, Running
Sequence Nodes (): Runs children one by one, from left to right. If one fails, the whole sequence fails. It only succeeds if all children succeed.
Fallback Nodes (?): Runs children one by one, from left to right. If one succeeds, the node stops and returns success. It only fails if all children fail.

## Slide 10: BT Nodes
Decorator Nodes – the Modifiers
Have exactly one child.
Change the child behavior
Inverter: Turns Success into Failure and vice versa
Repeater: Runs the child multiple times
Retry: Keeps ticking the child until it succeeds

## Slide 11: BT Nodes
Leaf Nodes – the Doers
Have no child.
Leaf Nodes interact with the robot or the environment
Action Nodes: Perform an actual task
Condition Nodes: Check a state without changing anything

## Slide 12: Components of BT
Blackboard: Shared memory space
Key – value database
Nodes are defined in C++ by users/developers
Nodes write and read values via Blackboard
Data Types: anything (Boolean, int, vector, vector3 …)

## Slide 13: BT Blackboard and Ports
Input port can read an entry in the Blackboard
Output port can write into an entry in Blackboard

## Slide 14: Implementing BT
BT (.xml)
Action Nodes (.cpp)
BT Factory
Register C++ Classes to match XML