## Slide 1: Priority-driven Scheduling
Lecturer: BuiHa Duc, PhD
Department of Mechatronics

## Slide 2: Deadline Monotonic Scheduling
DMS was first proposed in 1982 by Leung and Whitehead
DMS is an extension of RMS where task have relative deadline less than or equal to their period.
pi

## Slide 3: Deadline Monotonic Scheduling
DMS assigns task priority according to relative deadlines
  the shorter the relative deadline, the higher the priority
When relative deadline of every task matches its period, then rate monotonic and deadline monotonic give identical results
DMS can sometimes produce a feasible schedule in cases where rate monotonic cannot
RMS always fails when DMS fails
When deadline ≠ period, DMS is preferred

## Slide 4: SCHEDULABILITY ANALYSIS
Method 1: Utilization test (pessimistic)
Method 2: Reponse time analysis
DMS fails  RMS fail

## Slide 5: Example
Exam the schedulability of these tasks
 | Ci | Pi | Di
T1 | 1 | 4 | 5
T2 | 1 | 5 | 4
T3 | 2 | 6 | 5
T4 | 1 | 11 | 10

## Slide 6: DMS vs RMS

## Slide 7: Dynamic Priority Scheduling
Dynamic priority: priority of a task or job is not fixed but is calculated or adjusted at runtime
  Typically based on remaining time to deadline or slack time
Dynamic priority scheduling has higher utilization bound.
FreeRTOS is a fixed-priority, preemptive scheduler  does not implement dynamic priority scheduling by default.
  must calculate tasks’ priority periodically, then use vTaskPrioritySet() to manually update
  void vTaskPrioritySet( TaskHandle_t xTask, UBaseType_t uxNewPriority );

## Slide 9: Dynamic-Priority Algorithms
Core Dynamic Priority Algorithms
Earliest deadline first (EDF)
  The job queue is ordered by earliest deadline
Least slack time first (LST)
  The job queue is ordered by least slack time
  Scheduling decisions made only when jobs release or complete
First in, first out (FIFO)
  Job queue is first-in-first-out by release time
Last in, first out (LIFO)
  Job queue is last-in-first-out by release time

## Slide 10: Earliest deadline first (EDF)
EDF is the most well-known dynamic priority algorithm.
Priority Rule: The task with the earliest absolute deadline (di) is assigned the highest priority.
Schedulability Bound: A set of tasks is EDF-schedulable if and only if the total CPU utilization is less than or equal to 1

## Slide 11: Schedulability Tests: EDF
If Di < pi, use density test.
  Density of a task:
  Density of the system:
  A system T of independent, preemptable periodic tasks can be feasibly scheduled on one processor if Δ ≤ 1.

## Slide 12: Least Slack Time First
LST is an algorithm under the same basic conditions as EDF
Priority rule: The task with the least slack time (or laxity) is assigned the highest priority
Si(t) = (Absolute deadline – Current time) – Remain execution time
LST requires the scheduler to accurately track and update the remaining execution time for every task  significant runtime overhead and complexity
LST can suffer from a high number of context switches

## Slide 13: Optimality of EDF and LST
On a single processor, as long as preemption is allowed and jobs do not contend for resources, EDF and LST are optimal
  they will always produce a feasible schedule if one exists
  if they fail to produce a feasible schedule, no feasible schedule exists
Neither algorithm is optimal if jobs are non-preemptable or if there is more than one processor

## Slide 14: Example: Earliest Deadline First

## Slide 18: Practice considerations
Fixed- and dynamic-priority scheduling algorithms have different properties; neither appropriate for all scenarios
Algorithms that do not take into account the urgencies of jobs in priority assignment usually perform poorly (e.g FIFO, LIFO)
The EDF algorithm gives higher priority to jobs that have missed their deadlines than to jobs whose deadline is still in the future
Dynamic algorithms like EDF can produce feasible schedules in cases where RM and DM cannot
Fixed priority algorithms often more predictable, lower overhead

## Slide 19: Example: Comparing Different Algorithms
Assume a single processor system with 2 tasks
T1(2, 1)
T2(5, 2.5)
Total utilization is 1  no slack time
Try to schedule these tasks with RMS, EDF, LST, FIFO

## Slide 20: Example: Comparing Different Algorithms