## Slide 1: Priority-driven Scheduling
Lecturer: BuiHa Duc, PhD
Department of Mechatronics

## Slide 2: Assumptions
Priority-driven scheduling of periodic tasks on a single processor
There are no aperiodic or sporadic tasks
Scheduling decisions made immediately upon job release and completion
  Algorithms are event driven, not clock driven

## Slide 3: Priority-driven algorithms
A priority-driven scheduler is an on-line scheduler
  It does not pre-compute a schedule of tasks/jobs
  It assigns priorities to jobs when released, places them on a run queue in priority order
  At each scheduling decision time, the scheduler updates the run queues and executes the job at the head of the queue
Jobs in a task may be assigned the same priority (fixed priority) or different priorities (dynamic-priority)
The priority of each job is usually fixed

## Slide 4: Priority-driven algorithms
Advantages of priority-driven scheduling:
  Better suited to applications with varying time and resource requirements, since needs less a priori information
  Run-time overheads are small

## Slide 5: PreemPtion
Preemption is the act of an operating system (OS) interrupting a lower-priority task to run a higher-priority task that has become ready
High Priority Task
Low Priority Task
Time
Time
Preemption

## Slide 6: PreemPtion
Time
1. Trigger by interrupt
Higher Priority Task Arrival
Timer Expiration
2. Saving the context
CPU halt the running task (e.g. task A)
Current state is save into Process control Block (PCB)
3. Decision of scheduler
Interrupt handler notify the scheduler
The Scheduler analyzes the Ready Queue  select task which highest priority
4. Context Switch
OS load the new task context from PCB
CPU starts executing the new Task
5. Resume
Task A is move into ready queue
CPU will resume the task when its priority is the highest
Preemption relies on specific CPU hardware features

## Slide 7: Task Switching in FREERTOS
FreeRTOS scheduling policy
Fixed-priority: every task is assigned a priority, which does not change during runtime
Preemptive: always run the highest-priority task that is in the Ready state
Time Slicing: for tasks of equal priority, FreeRTOS switches between them on every RTOS Tick interrupt.
  Time slicing can be disabled using the configUSE_TIME_SLICING setting
Round-robin: tasks that share a priority take turns entering the Running state

## Slide 8: Task Switching in FREERTOS
In FreeRTOS, task preemption is triggered by one of three main events
PendSV Interrupt
  Software triggered, deferred context switch,
  Lowest priority PendSV will be executed when the CPU is free
SVC interrupt
  risen by SVC instruction
  SVC 0 call used only once, to start the scheduler (within vPortStartFirstTask() which is used to start the kernel)
RTOS tick (SysTick) interrupt
  When tick occurs, OS will check if any task is waiting  context switching

## Slide 9: Task Switching in FREERTOS
FreeRTOS Preemptive mode

## Slide 10: Task Switching in FREERTOS
FreeRTOS Cooperative mode

## Slide 11: Rate Monotonic Scheduling
Best known fixed-priority algorithm
Assigns priorities to tasks based on their periods pi
  The shorter the period, the higher the priority
  The rate (of job releases) is the inverse of the period, so jobs with higher rate have higher priority
For example:
  T1(4,1)  rate = 1/4
  T2(5,2)  rate = 1/5
  T3(20,5)  rate = 1/20
In FreeRTOS: set priority based on task periods and use vTaskDelayUntil() function to implement the periodic release
Relative priorities: T1 > T2 > T3

## Slide 12: Example

## Slide 13: Example
Visualization: https://ddmills.com/schedule-vis/

## Slide 14: Schedulability Tests: RMS
Method 1: (Liu and Layland, 1973)
Total utilization of the system:
where
In RMS: a system of n independent preemptable periodic tasks with Di= pi can be feasibly scheduled on one processor using RM if
ln(2)

## Slide 15: Schedulability Tests: RMS
If the relative deadlines for tasks are not equal to their respective periods
It can be shown that:

## Slide 16: Schedulability Tests: RMS

## Slide 17: Schedulability Tests: RMS
Method 2: Response Time Analysis (RTA)
The primary goal of RTA is to calculate the Worst-Case Response Time (Ri) for every task in the system
A task set is considered schedulable if and only if:
where:
: The set of all tasks with a Higher Priority than Ti
The Number of Times task Tj can preempt Ti during the response time Ri.
Blocking Time

## Slide 18: Example
  T1(4,1)  rate = 1/4
  T2(5,2)  rate = 1/5
  T3(20,5)  rate = 1/20
Liu & Layland analysis:
May not be schedulable
Response Time Analysis (RTA)
RTA for T1:  Schedulable
RTA for T2: only T1 can preempt T2
RTA for T3: T1 and T2 can preempt T3

## Slide 19: Example
RTA for T2
RTA for T3
 Schedulable
 Schedulable